Panstamp Heating etc control control codes

C0

Sleep or reset? Not yet implemented.

C1 Pn Hv

Set output n to v. n = 1 is the MOSFET. Outputs 2 to 6 are on the 7 pin header, which goes:

 +12v
 Gnd
 2 (Arduino D8)
 3 (Arduino D9) - Not available in LED control mode
 4 (Arduino A3 = D17)
 5 (Arduino A1 = D15)
 6 (Arduino A2 = D16)

C2

Return my temperature. When wireless requested this gives an integer in 0.1 degrees Celsius. From the serial interface it just gives degrees Celsius.

C3 An Ssome command

Send "some command" to device n

C4

Print/send firmware version number and address

C5 Pn Hv

Low level set Arduino pin n to value v. NB this also sets pin n to output mode.

C6 r0.7 g0.2 b0.1

Sets the LEDs to the rgb values specified in the range [0, 1].